## Slide 1: Basic Electrical and Electronics Engineering
Dr. Sonam Shrivastava/ Assistant Professor (Sr.) /SELECT
LECTURE 3.2

## Slide 2
BEEE102L
Basic Electrical and Electronics Engineering
DC Circuits
AC Circuits
Magnetic Circuits
Electrical Machines
Semiconductor Devices and Applications
Digital Systems

## Slide 3
Books
Text Books | 
Allan R. Hambley, “Electrical Engineering -Principles & Applications”, 2019, 6th Edition, Pearson Education | 
V. D. Toro, Electrical Engineering Fundamentals, 2nd edition. PHI, 2014 | 
Reference Books | 
R. L. Boylestad and L. Nashelsky, Electronic Devices and Circuit Theory, 11th edition. Pearson, 2012 | 
DP Kothari & Nagrath, “Basic Electric Engineering”, 2019, Tata McGraw Hill | 

## Slide 4: Module 3. Magnetic Circuits
Magnetic field; Toroidal core: Flux density, Flux linkage;
Magnetic circuit with air gap;
Reluctance in series and parallel circuits;
Electromagnetic Induction: Self And Mutual
Magnetically Coupled Circuits
Series and Parallel Magnetic Circuits
Dot Convention

## Slide 5
MAGNETIC CIRCUITS
A magnetic circuit is defined as a closed path followed by the magnetic flux.
Consider a coil of N turns wound on an iron core (see the figure).
When an electric current I is passes through the coil, magnetic flux (ψ) is set up in the core.
This magnetic flux follows a closed path ABCDA and hence ABCDA is the magnetic circuit.
In a magnetic circuit, the amount of magnetic flux in the core depends upon the current (I) and the number of turns (N).
The product NI is known as the Magneto motive Force (MMF).
      MMF=NI=Ampere−Turns
The opposition offered by the magnetic circuit to the flow of magnetic flux is known as reluctance (S) of the magnetic circuit.

## Slide 6
MAGNETIC CIRCUITS
Series Magnetic circuit
    Simple magnetic circuit
    Composite magnetic circuit
Parallel Magnetic circuit
Series and parallel magnetic circuit

## Slide 7
Simple SERIES MAGNETIC CIRCUITS

## Slide 8
Simple SERIES MAGNETIC CIRCUITS

## Slide 9
Composite series magnetic circuits
When the same magnetic flux ψ flows through each part of the magnetic circuit, then the circuit is called as series magnetic circuit.
Consider a composite series magnetic circuit (a series magnetic circuit that has parts of different dimensions and materials is called a composite series magnetic circuit) consisting of three different magnetic materials of different relative permeability.
Each part of this series magnetic circuit will offer reluctance to the magnetic flux ψ. Since the different parts of the magnetic circuit are in series, the total reluctance is equal to the sum of reluctances of individual parts.

## Slide 10
Current I is passed through the solenoid having N number of turns wound on the one section of the circular coil. Φ is the flux, set up in the core of the coil.
Composite series magnetic circuits
Cross-sectional area of the solenoids= a1, a2, a3
Length of the three different coils having different dimension joined together in series= l1, l2, l3
Relative permeability of the material of the circular coils= µr1, µr2, µr3 .
ag =Area of the air gap
lg =Length of the air gap.

## Slide 11
Composite series magnetic circuits

## Slide 12
Composite series magnetic circuits
Using
in eq 2

## Slide 13
Problem 1. A magnetic circuit consists of an iron ring of mean circumference 80 cm with cross-sectional area of 12 cm2 throughout. A current 0f 2A in the magnetising coil of 200 turns produces a total flux of 1.2 mwb in the iron. Calculate :
(i) the flux density in the iron
(ii) the absolute and relative permeability's of iron.
(iii) the reluctance of the circuit.

## Slide 14
Problem 1. A magnetic circuit consists of an iron ring of mean circumference 80 cm with cross-sectional area of 12 cm2 throughout. A current 0f 2A in the magnetising coil of 200 turns produces a total flux of 1.2 mwb in the iron. Calculate :
(i) the flux density in the iron
(ii) the absolute and relative permeability's of iron.
(iii) the reluctance of the circuit.
B=1 wb/m2
AT/Wb

## Slide 15
Problem 1. A magnetic circuit consists of an iron ring of mean circumference 80 cm with cross-sectional area of 12 cm2 throughout. A current 0f 2A in the magnetising coil of 200 turns produces a total flux of 1.2 mwb in the iron. Calculate :
(i) the flux density in the iron
(ii) the absolute and relative permeability's of iron.
(iii) the reluctance of the circuit.
B=1 wb/m2
AT/Wb