## Slide 1: Basic Electrical and Electronics Engineering
Dr. Sonam Shrivastava/ Assistant Professor (Sr.) /SELECT
LECTURE 1.1

## Slide 3
BEEE102L
Basic Electrical and Electronics Engineering
DC Circuits
AC Circuits
Magnetic Circuits
Electrical Machines
Semiconductor Devices and Applications
Digital Systems

## Slide 5
Books
Text Books | 
Allan R. Hambley, “Electrical Engineering -Principles & Applications”, 2019, 6th Edition, Pearson Education | 
V. D. Toro, Electrical Engineering Fundamentals, 2nd edition. PHI, 2014 | 
Reference Books | 
R. L. Boylestad and L. Nashelsky, Electronic Devices and Circuit Theory, 11th edition. Pearson, 2012 | 
DP Kothari & Nagrath, “Basic Electric Engineering”, 2019, Tata McGraw Hill | 

## Slide 6: Module I. DC Circuits
Source transformation
Super position theorem

## Slide 7: Electrical Circuits
A circuit consists of electrical elements connected together.
Example.

## Slide 8: Electric Charge
Definition: Electric charge is a basic property of electrons, protons and other subatomic particles.
The quantity of electricity that flows in a given time or is held in a component such as a capacitor.
Symbol: q or Q
Unit: Coulomb (C)
Notes: Charges may be positive or negative
Like charges (e.g., + and +) repel each
other, unlike charges (+ and -) attract
each other

## Slide 9
Electric Current
Definition: Rate of positive charge flow
Symbol: i or I
Units: Coulombs per second ≡ Amperes (A)
i = dq/dt
where q = charge (in Coulombs), t = time (in seconds)
Note: Current has polarity (flow direction).
If the drift of electrons in a conductor takes place at the rate of one coulomb per second the resulting current is said to be a current of one ampere.

## Slide 10
Electric Potential (Voltage)
Definition: The work required to move a unit charge from a reference point to a specified point is voltage, measured in joules per coulomb or volts.
Symbol: v
Units: Joules/Coulomb ≡ Volts (V)
v = dw/dq
where w = energy (in Joules), q = charge (in Coulombs)
Note: Potential is always referenced to some point.
Subscript convention:
vab means the potential at a minus the potential at b.
a
b
vab = va - vb

## Slide 11
Electric Power
Definition: amount of energy transferred per unit time.
Symbol: p or P
Units: Joules per second ≡ Watts (W)