## Slide 1: Basic Electrical and Electronics Engineering
Dr. Sonam Shrivastava/ Assistant Professor (Sr.) /SELECT
LECTURE 1.3

## Slide 2: Module I. DC Circuits
Source transformation

## Slide 3
Kirchhoff’s Laws
Kirchhoff’s Current Law (KCL):
  The algebraic sum of all the currents entering any node in a circuit equals zero. (An expression of the conservation of charge.)
Kirchhoff’s Voltage Law (KVL):
  The algebraic sum of all the voltages around any loop in a circuit equals zero. (As a result of conservation of energy.)

## Slide 4
Kirchhoff’s current Law
  The algebraic sum of all the currents entering any node in a circuit equals zero. (An expression of the conservation of charge.)
  The algebraic sum of all the currents leaving any node in a circuit equals zero.
  Sum of all the incoming currents = Sum of all the outgoing currents.
  Reference direction conventions:
  Treat all outgoing currents as +ve
  Treat all incoming currents as -ve

## Slide 5
Use reference directions to determine whether currents are “entering” or “leaving” the node – with no concern about actual current directions
i1
i4
i3
i2
Consider a node connecting several branches:
Using Kirchhoff’s Current Law (KCL)

## Slide 6
KCL example

## Slide 7
A Major Implication of KCL
KCL tells us that all of the elements in a single branch carry the same current.
We say these elements are connected in series.
Current entering node = Current leaving node
i1 = i2

## Slide 8
(Conservation of energy)
Formulations of Kirchhoff’s Voltage Law
  Reference direction conventions:
  Treat all voltage drops as -ve
  Treat all voltage gains as +ve
Algebraic sum of voltage drops around loop = 0

## Slide 9
Use reference polarities to determine whether a voltage is dropped – with no concern about actual voltage polarities
Consider a branch which forms part of a loop:
+
v1
_
loop
voltage
“drop”
–
v2
+
loop
voltage
“rise”
(negative drop)
Using Kirchhoff’s Voltage Law (KVL)

## Slide 10
Find , , ,

## Slide 11
KVL Example

## Slide 12
KVL Example

## Slide 13
KVL Example

## Slide 14
Path 1:
Path 2:
Path 3:
vc
va
+

+

3
2
1
+ 
vb
v3
v2
+ 
+
-
Three closed paths:
a
b
c
KVL Example